## Slide 1: Laboratory 2
The conduction system of the heart and electrocardiography

## Slide 2: Lab 2 Activities
Anatomy of the internal conduction pathway of the heart.
Biopac Exercise L05-ECG-1: Normal electrocardiogram (including the names of all waves, intervals, and segments, what they mean, and how they correlate to the parts of the cardiac cycle).

## Slide 3: Conduction System and Pacemakers
Autorhythmic cells
  Cardiac cells repeatedly fire spontaneous action potentials
  Autorhythmic cells: the conduction system
  Pacemakers
    SA node
      origin of cardiac excitation
      fires 60-100/min
    AV node
    conduction system
      AV bundle of His
      R and L bundle branches
      Purkinje fibers
It’s as if the heart had only two motor units: the atria and the ventricles!

## Slide 4
Caution: Electrode clips are fragile; place cords where they will not be stepped on, in use, or when you are through!
The ECG: Electrode Placement

## Slide 5: The ECG
Below are illustrated the waves (deflections) of a typical cardiac cycle.
P
R
Q
S
T

## Slide 6: The ECG
Waves, intervals and segments of one cardiac cycle are illustrated below.
PR (PQ)
Interval
ST
segment
QT interval
P
Q
R
S
T
QRS complex

## Slide 7: BIOPAC NOTES
During calibration:
  The subject should be sitting still, hands resting in lap or on knees- click Calibrate
  If the beginning of the baseline is decreasing, redo the calibration.
  The baseline should be more or less constant (horizontal) during calibration.

## Slide 8: BIOPAC NOTES
During data collection (record – suspend – resume)
  Treatment 1: Supine the bench top or three chairs or at least with feet elevated in a second chair; arms folded across waist if prone; breathing normally
  Click Record , after 20 seconds click Suspend
  Treatment 2: Sitting in a chair with arms at sides, hands in lap, feet on the floor and breathing normally
  Click Resume , after 20 seconds click Suspend
  --Treatment 3: Still seated, click on Resume as subject inhales and exhales deeply for 5 prolonged breath cycles. Recorder must press F4 at start of each inhale and F5 at start of each exhale. After the five breaths, record 5 more seconds then click Suspend
  Treatment 4:Exercise vigorously for 1 minute- heart rate should be elevated. As soon as subject is seated click on Resume for 5 minutes.
  Click Done. Choose “Record from another subject”, when each person is done then choose “Analyze current data”.
  Click “Review Saved Data”- find the “Data files” folder and your data with the ECG tracing.

## Slide 9: BIOPAC NOTES
Data Analysis
  Ensure the boxes at the top are as depicted by the red arrow
  Magnify image so that 2-3 cardiac cycles are visible.

## Slide 10: BIOPAC NOTES
  Measure how long each event lasted
  Delta T: Delta = Change, T = Time
  The PR interval (PQ interval) is measured from the start of the P wave (not the top of P) to the start of the Q wave, but we will use Q, which is easier to identify

## Slide 11: BIOPAC NOTES
  Measure how long each event lasted
  Be sure that you analyze and record results of 2 cardiac cycles for each treatment in your lab manual.
    Tables 1 and 2, page 2-7
  Calculate the average of the 2 cycles!
  Do not select cardiac cycles that are right next to each other.
  Do your best to identify wave transitions. Be consistent!

## Slide 12: BIOPAC NOTES
Measure the BPM for the same two cardiac cycles for each procedure
  Use the I-beam to highlight one cardiac cycle and measure from the top of R to the top of R of the next cycle (R to R) to record the beats per minute rate for each treatment
  Record results from 2 cardiac cycles for each treatment segment in Tables 1 and 2.
  Calculate the average of the 2 cycles!

## Slide 13: BIOPAC NOTES
Cardiac Cycle
  Calculate by summing the appropriate intervals.
Rounding
  Round your Delta T values for intervals and segments to two decimal places, e.g., 0.16.
  Round your BPM values for Heart Rate to one decimal place, e.g., 72.1.

## Slide 14: Your Assignment
Print a representative section (2-3 cardic cycles) of your ECG for the first set of treatment data (supine).
Label the waves, intervals, and segments of a typical cardiac cycle on the ECG you print.
Fill in Tables 1 & 2 as you analyze your data on page Lab 2-7 of your lab manual.
Answer the questions on page Lab 2-8.
No on-line homework this week.

## Slide 15: BIOPAC NOTES
Your graph should look like this.
Then be sure you label the waves (P, Q-R-S, and T), intervals and segments (PR, ST, and QT) on the graph.

## Slide 16: End Lab 2